## Slide 1
A Mobile Sensor Network to Map CO2 in Urban Environments
Joey Lee1, Andreas Christen1, Zoran Nesic2, & Rick Ketler1
Department of Geography1
Department of Land and Food Systems2
The University of British Columbia
9th International Conference on Urban Climate
Toulouse, France
July 24, 2015

## Slide 2
Overview
We present a pilot study to show the potential for a mobile sensor network to monitor greenhouse gas concentrations and to derive emissions in cities.

## Slide 3
Can we map greenhouse gases, specifically CO2, at a spatial resolution of neighborhoods / blocks across the city with a network of mobile sensors?
Research Question

## Slide 4
Motivations: Why Mobile Sensing?

## Slide 5
Motivations: Why Mobile Sensing?
Cities are a major source of GHGs into the atmosphere (Estimated 70%, Rosenzweig 2010).

## Slide 6
Motivations: Why Mobile Sensing?
Cities are a major source of GHGs into the atmosphere (Estimated 70%, Rosenzweig 2010).
  Currently there are a lack of tools to monitor CO2 emissions in cities; existing tools are limited by funding, time, expertise, spatial & temporal resolution.

## Slide 7
Motivations: Why Mobile Sensing?
Cities are a major source of GHGs into the atmosphere (Estimated 70%, Rosenzweig 2010).
  Currently there are a lack of tools to monitor CO2 emissions in cities; existing tools are limited by funding, time, expertise, spatial & temporal resolution.
  There’s a need to validate fine scale emissions inventories.

## Slide 8
Motivations: Why Mobile Sensing?
Cities are a major source of GHGs into the atmosphere (Estimated 70%, Rosenzweig 2010).
  Currently there are a lack of tools to monitor CO2 emissions in cities; existing tools are limited by funding, time, expertise, spatial & temporal resolution.
  There’s a need to validate fine scale emissions inventories.
Emerging Opportunities...
Rise of flexible (open source), compact technologies.
Enhanced access to mobility services/platforms

## Slide 9: But how do you go from concentrations to emissions?

## Slide 10
Proposed Approach: Using the aerodynamic
resistance (with a number of assumptions!)
Sensible heat flux & temperature are used to calculate the aerodynamic resistance for heat. Surface temperature is calculated with a radiometer at the surface. Assuming that that the aerodynamic resistance of CO2 and heat are the same, the flux is computed.
Notes: Ro = density of dry air
Cp = specific heat of air

## Slide 11: The Mobile Sensor System

## Slide 12
System Components
1. IRGA – Licor LI-820 (Licor Inc, Lincoln, NB, USA), 2. Adafruit GPS (Adafruit Industries, Manhattan, NY, USA), 3. Arduino Mega (Arduino CC, Ivrea, Italy) . *Not Shown: OneWire Digital Temperature Thermometer (Maxim Integrated One Wire Digital Temperature Sensor - DS18B20, San Jose, CA, USA )

## Slide 13
System Specifications

## Slide 14
Runs on 12 V Power supply
System Specifications

## Slide 15
Runs on 12 V Power supply
Measures CO2 mixing ratios (ppm), geoposition and speed, and air temperature at 1-second intervals.
System Specifications

## Slide 16
Runs on 12 V Power supply
Measures CO2 mixing ratios (ppm), geoposition and speed, and air temperature at 1-second intervals.
Size: 35.8 cm x 27.8 cm x 11.8 cm, weight: 2.6 kg.
System Specifications

## Slide 17
Runs on 12 V Power supply
Measures CO2 mixing ratios (ppm), geoposition and speed, and air temperature at 1-second intervals.
Size: 35.8 cm x 27.8 cm x 11.8 cm, weight: 2.6 kg.
Precision: +/- 1.1 ppm
System Specifications

## Slide 18
Runs on 12 V Power supply
Measures CO2 mixing ratios (ppm), geoposition and speed, and air temperature at 1-second intervals.
Size: 35.8 cm x 27.8 cm x 11.8 cm, weight: 2.6 kg.
Precision: +/- 1.1 ppm
Accuracy: +/- 3 ppm, with maximum drift of +/- 4 ppm over seven days.
System Specifications

## Slide 19
Runs on 12 V Power supply
Measures CO2 mixing ratios (ppm), geoposition and speed, and air temperature at 1-second intervals.
Size: 35.8 cm x 27.8 cm x 11.8 cm, weight: 2.6 kg.
Precision: +/- 1.1 ppm
Accuracy: +/- 3 ppm, with maximum drift of +/- 4 ppm over seven days.
Total delayed response time: 13 s with 3 m sample tube at flow rate of 700 cc/min.
System Specifications

## Slide 20
Built & Tested: 5 mobile systems
Image: In total 5 sensors were built – the image shows the full setup including the sample inlet tube and the temperature probes.

## Slide 21: Mapping Emissions – Methods: Measurement Campaign
May 25th, 2015

## Slide 22
Study Area: 12.7 km2 transect, Vancouver, BC
Image: 12 km2 transect study area in Vancouver, BC. The transect is 1km x 12.7km covering the major land cover types in the city. Sunset Urban Climate tower is shown in orange.
Notes: Put location of flux tower!!!

## Slide 23
Study Area: Tour of Vancouver
Video: A tour of Vancouver during the measurement campaign as seen through a dashboard camera. Local climate zones include Forest – A, compact midrise, compact high rise, compact lowrise, and open lowrise
Notes: (add video)

## Slide 24
Measurement period: 10:30 – 14:00
With convective and steady weather
  Tair = 20° - 22° C
  Winds: 2.5 m/s
  Cloudless
* data measured at 30m Urban Climate Tower "Vancouver Sunset" (SE section of Transect)
Study Area: Meteorology - May 25th, 2015

## Slide 25
Sampling Methods: Vehicle Installation
Image A: Shows the temperature probe covered by PVC tube and reflective tape and sample inlet tube at 2m height - ±0.5°C Accuracy from -10°C to +85°C ; Image B: Shows sensor installation in vehicle.

## Slide 26
Sampling Methods: Bike Installation
Image: Shows the installation of the sensor on a bike rack – the inlet is at approximately 2m height.

## Slide 27
Sampling Methods: Deployment Transects
Image: The image shows 5 planned transect routes for the measurement campaign. Goal: to cover (almost) all navigable roads (and some trails) along the transect in 3.5 hours.

## Slide 28: Pilot Study - Mapping CO2 Emissions: Results

## Slide 29
Raw Data: Visualized in Google Earth

## Slide 30
Average CO2 Mixing Ratios per 100m Grid Cell
Notes: Figure out which graph to put
Take out skewness!

## Slide 31
Calculated Emissions: Concentrations to Emissions
Image: Calculated emissions map generated using the aerodynamic resistance approach using CO2 concentration measurements.

## Slide 32: Mapping Emissions – Methods: Emissions Inventory

## Slide 33
Image: The traffic emissions inventory derived from Vancouver’s traffic count data and calculated per grid cell using fuel consumption and emissions factors.
Traffic Emissions Inventory

## Slide 34
Building Emissions Inventory
Image: Building emissions inventory generated by combining factors of building morphology, urban context, and population density derived from LiDAR, building topology, and census data.

## Slide 35
CO2 Mixing Ratios Vs. Traffic Emissions Inventory

## Slide 36
CO2 Mixing Ratios Vs. Total Emissions Inventory

## Slide 37
Calculated CO2 emissions vs. Traffic Emissions Inventory

## Slide 38
Calculated CO2 emissions vs. Building Emissions Inventory

## Slide 39
Calculated CO2 emissions vs. Total Emissions Inventory

## Slide 40
Conclusions & Future Directions

## Slide 41
A mobile CO2 sensing system was developed using opensource components.
Conclusions & Future Directions

## Slide 42
A mobile CO2 sensing system was developed using opensource components.
The system was tested in Vancouver and evaluated against traffic and building emissions inventories.
Conclusions & Future Directions

## Slide 43
A mobile CO2 sensing system was developed using open source components.
The system was tested in Vancouver and evaluated against traffic and building emissions inventories.
The study shows the potential for pervasive mobile sensing in GHG and pollutant monitoring in cities.
Conclusions & Future Directions

## Slide 44
A mobile CO2 sensing system was developed using open source components.
The system was tested in Vancouver and evaluated against traffic and building emissions inventories.
The study shows the potential for pervasive mobile sensing in GHG and pollutant monitoring in cities, but relies on specific conditions and assumptions.
Conclusions & Future Directions

## Slide 45
A mobile CO2 sensing system was developed using open source components.
The system was tested in Vancouver and evaluated against traffic and building emissions inventories.
The study shows the potential for pervasive mobile sensing in GHG and pollutant monitoring in cities, but relies on specific conditions and assumptions.
Currently exploring visualization & feedback opportunities for planning and open science.
Conclusions & Future Directions

## Slide 46
A mobile CO2 sensing system was developed using open source components.
The system was tested in Vancouver and evaluated against traffic and building emissions inventories.
The study shows the potential for pervasive mobile sensing in GHG and pollutant monitoring in cities, but relies on specific conditions and assumptions.
Currently exploring visualization & feedback opportunities for planning and open science.
Collaboration potential with local mobility providers for long term & spatially extensive/intensive monitoring
Conclusions & Future Directions

## Slide 47
NSERC Discovery Grant
NSERC CREATE - Terrestrial Ecosystems Research and World Wide Education & Broadcast Program (TerreWEB).
UBC Geography Department, Ron Kellett, & Les Lavkulich
Benedikt Groß, 47Nord GmBH, & Moovel Labs
Measurement Campaign Drivers: Alex McMahon, Andreas Christen, Mark Richardson, & Thea Rodgers.
ICUC & IAUC
Data: OpenStreetMap.org, Vancouver Open Data, EPiCC Project, UBC Micrometeorology
Tools: Python, R, QGIS, GDAL/OGR, Processing
Acknowledgements & Funding
References
Van der Laan, "Scaling Urban Energy Use and Greenhouse Gas Emissions through LiDAR", MSc Thesis, 2011.
Rosenzweig, C., Solecki, W., and Hammer, S. A. (2010). Cities lead the way inclimate-change action. Nature, pages 1–3.

## Slide 48
Special thanks to Andreas, Zoran, and Rick.

## Slide 49
The slides & links can be found on github:
joeyklee.github.io/presentations/ICUC-JLEE-2015

## Slide 50
Thanks!
Questions? Comments?
Many thanks to ICUC organizers and community.

## Slide 52
Methods: Multipoint Calibration
Image: Multipoint Calibration of Sensor System showing observed values versus known concentrations.

## Slide 53
Methods: Sensor Drift
Image: Testing for sensor drift of the five mobile sensors over a seven-day measurement period. Each line corresponds to one of the five mobile CO2 sensors.

## Slide 54
Study Area: Local Climate Zones
Image: The images above show typical urban features characteristic for each neighborhood in the study area and were taken with a dashboard camera during the measurement campaign.
Notes: (add video)

## Slide 56
Calculated Emissions Map
Image: Calculated emissions map generated

## Slide 57
Observed Mixing Ratios: Average & Median
per 100m grid cell by neighborhood
Notes: Figure out which graph to put

## Slide 58: An Aerodynamic Resistance Approach: From Concentrations to Emissions